## Slide 1
Digital Electronics
Class X
lab 19

## Slide 2
Decoder
Decoder is a combinational circuit that has ‘n’ input lines and maximum of 2n output lines.

## Slide 3
Input and Output for Basic Logic Gates

## Slide 4
Truth Table
Truth table is a tabular representation of all the combinations of values for inputs and their corresponding outputs.
A | B | AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5
2 to 4 Decoder
Let 2 to 4 Decoder has two inputs A1 & A0 and four outputs Y3, Y2, Y1 & Y0. The block diagram of 2 to 4 decoder is shown in the following figure

## Slide 6
Truth Table for 2 to 4 Decoder
Enable | Inputs |  | Outputs |  |  | 
E | A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | x | x | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 7
2 to 4 Decoder Diagram

## Slide 8
Thank You